## Slide 1: Assurance Management
Course Architect: Robert Ellison
This material was created with support and funding from

## Slide 2
Copyright 2014 Carnegie Mellon University This material has been approved for public release and unlimited distribution except as restricted below. This material is based upon work funded and supported by Department of Homeland Security under Contract No. FA8721-05-C-0003 with Carnegie Mellon University for the operation of the Software Engineering Institute, a federally funded research and development center sponsored by the United States Department of Defense. References herein to any specific commercial product, process, or service by trade name, trade mark, manufacturer, or otherwise, does not necessarily constitute or imply its endorsement, recommendation, or favoring by Carnegie Mellon University or its Software Engineering Institute. NO WARRANTY. THIS CARNEGIE MELLON UNIVERSITY AND SOFTWARE ENGINEERING INSTITUTE MATERIAL IS FURNISHED ON AN “AS-IS” BASIS. CARNEGIE MELLON UNIVERSITY MAKES NO WARRANTIES OF ANY KIND, EITHER EXPRESSED OR IMPLIED, AS TO ANY MATTER INCLUDING, BUT NOT LIMITED TO, WARRANTY OF FITNESS FOR PURPOSE OR MERCHANTABILITY, EXCLUSIVITY, OR RESULTS OBTAINED FROM USE OF THE MATERIAL. CARNEGIE MELLON UNIVERSITY DOES NOT MAKE ANY WARRANTY OF ANY KIND WITH RESPECT TO FREEDOM FROM PATENT, TRADEMARK, OR COPYRIGHT INFRINGEMENT. This material is distributed by the Software Engineering Institute (SEI) only to course attendees for their own individual study. Except for the U.S. government purposes described below, this material SHALL NOT be reproduced or used in any other manner without requesting formal permission from the Software Engineering Institute at permission@sei.cmu.edu. The U.S. Government's rights to use, modify, reproduce, release, perform, display, or disclose this material are restricted by the Rights in Technical Data-Noncommercial Items clauses (DFAR 252-227.7013 and DFAR 252-227.7013 Alternate I) contained in the above identified contract. Any reproduction of this material or portions thereof marked with this legend must also reproduce the disclaimers contained on this slide. Although the rights granted by contract do not require course attendance to use this material for U.S. Government purposes, the SEI recommends attendance to ensure proper understanding. CERT® is a registered mark of Carnegie Mellon University. DM-0001287

## Slide 3
Author of Module or CERT Program Month 2014
Assurance Management
Module 8
Assurance for Building Security In

## Slide 4
Assurance for Building Security In

## Slide 5: Outline
Open Group: Supply chain provider standard
Open Group: Accreditation: an assurance case
Applying assurance to outsourced development
Assurance: Government regulations and supply chain requirements

## Slide 6: Business Driver: Globalization of Supply Chains
Gain visibility into the risks inherent in global sourcing for product development and manufacturing by answering questions such as
  What potential security risks may be inherited from supply chains, both for software and hardware, and how does the Original Equipment Manufacturer (OEM) assess and manage these risks?
  What supply chain security practices can mitigate potential risks of significant supply chain attacks?
  What are the risks to confidentiality, integrity, and availability of a customer’s environment or critical infrastructure as a result of procurement by customers of counterfeit components and products?
  What software or technology development or engineering practices can help reduce product integrity risks?
  How is product integrity and risk managed through the adoption of industry best practices and assurance programs?

## Slide 7: Context-1
The Open Group Trusted Technology Forum created the supply chain provider certification process.
The working groups members were employees of major COTS suppliers as well as some representation for US Federally Funded Research and Development Centers such as MITRE and the SEI.

## Slide 8: Context-2
Motivations
  It is to the suppliers’ advantage to only have to show that their development/manufacturing practices satisfy an accepted standard for a level of supply chain risk management practices
  The COTS developers/manufactures have development/manufacturing practices customized to specific products – changes in company development lifecycles not a viable option.
    COTS suppliers must manage costs to remain competitive.
    An assessment should verify the output of the practices, i.e. what was done and how well it was done and not how it was done.
    Solution: evidence-based claims.

## Slide 9: Open Group Trusted Technology Forum
The Open Group has established an accreditation for supply chain risk management for COTS suppliers.
  The hazard is that hardware or software component has been malicious modified.
    Counterfeit hardware or integrated components
      Over 10 percent of government purchases are counterfeit.
      Several incidents of counterfeit CISCO routers.
    Firmware modified during manufacturer or in transit.
  Supply chains are complex:
    In a DoD counterfeit example a trace of supply chain participants went through five states and three countries to the final source which was known to provide counterfeits.
    Suppliers have to manage these risks.

## Slide 10: Open Trusted Technology ProviderTM Standard (O- TTPS)
The initial release of the standard addresses risks related to
  maliciously tainted product – the product is produced by the provider and is acquired through a provider’s authorized channel, but has been tampered with maliciously.
  counterfeit product – the product is produced other than by, or for, the provider, or is supplied to the provider by other than a provider’s authorized channel and is presented as being legitimate even though it is not.
But many of the requirements also address the risk of
  A software product containing inadvertently created software weaknesses that could be exploited.

## Slide 11: O-TTPS Constraints
COTS suppliers
  low cost so smaller firms can afford it.
  applicable to hardware and software supply chains
  certification is for products but too expensive to assess individual products. Some suppliers have over 800 products
    a certification is done for one or more products and applies to all products developed with the same practices

## Slide 12: Outline
Open Group: Supply chain provider standard
Open Group: Accreditation: an assurance case
Applying assurance to outsourced development
Assurance: Government regulations and supply chain requirements

## Slide 13: O-TTPS Scope
Applies to
  Technology Development: internal development
    product development/engineering method
    secure development/engineering method
  Supply Chain: Outsourced development
    third-party hardware and software
    outsourced development and manufacture

## Slide 14: Open Group O-TTPS Content
Containing a set of guidelines that have been shown to enhance
  the security of the global supply chain
  integrity of COTS Information Communication and Technology (ICT) products.
Covers design, sourcing, build, fulfillment, distribution, sustainment, and disposal.

## Slide 15: Open Group: Accreditation
Create a process that can certify that an organization practices meet the standard.
The certification process is equivalent to assurance case analysis of an organization’s COTS life cycle practices
  The standard provides subclaims in the form of guidelines, requirements, and recommendations.
  It suggests evidence that can demonstrate that subclaims have been satisfied.
  The subclaims and suggested evidence provide the means for an independent laboratory to do the analysis required to justify the certification.

## Slide 16: An Assessment Requires an Assurance Argument and Evidence
Supplier employees are educated in security engineering practices
All engineers are educated and trained.
Training is updated sufficiently frequently
Appropriate experts teach each of the classes
Documentation for each engineer of the training received and the date when trained/retrained.
Revision dates for training materials
List of acceptable credentials for instructions
Names of instructors and their credentials.

## Slide 17: Technology Development
Product Development/Engineering Method – BSIMM also
  well- defined, documented, and repeatable product development or engineering method and/or process
  effectiveness of the method is managed through metrics and management oversight.
Secure Development/Engineering Method
  software providers
    employ methods or processes with the objective of identifying, detecting, fixing, and mitigating defects and vulnerabilities
    verify the security and resiliency of the finished products.
  hardware providers
    mitigate use of unverified and inauthentic software
    protect against counterfeit hardware or software

## Slide 18: Threat Analysis and Mitigation-1
What you would like to find:
  has identified a set of potential attacks and how they could be executed
  has described how those attacks could be best prevented or mitigated
  has assessed product architecture and design against potential attacks
  the threat analysis is used to design test plans
    evidence-based: test plans include
      potential attacks patterns
      likely occurring software weaknesses: example fuzz testing for inputs
      mitigations and security controls incorporated in software

## Slide 19: Threat Analysis and Mitigation-2
Evidenced-based
  documentation of architecture and design processes
  a list of known potential attacks.
  reports on threat assessments done against architecture and design
  reports on vulnerability analysis done during all phases
  process documentation for creation of test plans
  a sample of test plans and results

## Slide 20: Vulnerability Analysis and Response
What you would like to find.
  techniques such code review, static analysis, penetration testing, white/black box testing are used for vulnerability analysis.
    evidence-based
      The attacks identified in the attack analysis are included in the vulnerability analysis: code scanning reports, code review reports
  vulnerability analysis and response feeds into the processes for ongoing product development, product patching, and remediation.

## Slide 21: Secure Engineering Practices
What you would like to find.
  secure coding practices such as input validation and use of appropriate compiler flags are used to avoid common coding errors – also in BSIMM
    evidence-based
      acceptable coding patterns, execution is shown from output from tools that enforce coding patterns, or from reports on manual code reviews

## Slide 22: Evolution of Development Practices
What you would like to find.
  changes to the threat landscape are monitored periodically.
  development/engineering practices, tools, and techniques are assessed and changed based on
    changes in the threat landscape
    the causal analysis of a new vulnerability in order to mitigate future occurrences

## Slide 23: Will Anyone Use It?
Public Announcement 2/2014
The target was what might be considered a medium level or acceptable level of assurance for COTS suppliers.
  COTS market place does not include high-assurance software
  A certification has to be realistic for most COTS suppliers.
Success depends on
  Is there a market need “medium level assurance”? Vendors will seek certifications only if required by acquirers.
  Will certified suppliers have supply chain risks that are considered to be acceptable for sufficiently large group of acquirers?

## Slide 24: Outline
Open Group: Supply chain provider standard
Open Group: Accreditation: an assurance case
Applying assurance to outsourced development
Assurance: Government regulations and supply chain requirements

## Slide 25: Requiring Assurance For Supply Chains
Organization
Computational service
Develop In-house
Assurance of product and of vendor capabilities
Acquire (COTS)
Internal Development
Assurance of system and of team capabilities
Outsource Development
Outsource to external service provider
Assurance of service and of provider capabilities
Role of your organization
Assurance of system and of contractor capabilities
Notes: Let's say the objective is to build a software system.
In this instance, the acquirer has a program office that manages the selection of a prime contractor and monitors the development of the system. The supply chain appears to be simple: program office and prime contractor, but the supply chain for a system acquisition is complex.
The prime contractor has multiple kinds of supply chains. A large system usually includes commercial software products including what we call commercial off-the-shelf or COTS software. Those developers have supply chains.
A prime contractor’s internal software development can be done at multiple locations in the U.S. and offshore.
A prime contractor usually has subcontractors who can be geographically distributed and may have their own supply chains.
It is not unusual for a large system to reuse existing software. But enough time has passed that our knowledge of those efforts is incomplete compared to that for current development.
We also have a collection of supply chain threats. Some of the hardware items could be counterfeit or have been the subject of tampering.
There can be software components with weaknesses that an attacker can exploit to compromise a system, and we have a special class of software called firmware that controls the behavior of electronic devices that might have been replaced.

## Slide 26: What Should We Look For?
Business risks and attack surface analysis continues throughout life cycle. In particular such analysis should have guided top-level design decisions.
Security and assurance check points have been identified at various points in the life cycle
  Higher levels of assurance can require explicit measures at the check points and that exceptions are tracked.
  Such a requirement is supported by the 2011 version of the DoD Program Protection Plan and is a BSIMM Level 1 activity
Notes: STUDENT NOTES

## Slide 27: Examples of Early Life Cycle Activities Checks
Have the security risks associated with system functionality (What we want) and with the proposed system implementation (How we build it) been identified?
  Developer knowledgeable of threats and attack enablers
  Developer is aware of the effects of system requirements and design decisions on security and mission threads (operations).
Notes: STUDENT NOTES

## Slide 28: Examples of Middle Life Cycle Checks: 1
Are the appropriate standards and requirements in place for development
  There are security standards include those for secure coding.
  Security standards are shared with vendors and subcontractors.
  Do the vendors and subcontractors follow those standards?
What are the requirements for required security controls?
  Application input monitoring will be employed.
  The production software will be monitored for misbehavior and signs of attack.
Notes: STUDENT NOTES

## Slide 29: Examples of Middle Life Cycle Checks: 2
Which failure conditions have the highest priority? How will those conditions be managed?
Have testing personnel participated in risk analysis and design work?
  Likely failure conditions have to be incorporated into the test plan.
  A software design requires bounds on the operating conditions. Testing should test those boundary conditions.
Notes: STUDENT NOTES

## Slide 30: Examples of Late Life Cycle Activities Checks-1
What are the results of the code reviews?
Which system boundary conditions been tested.
  The tested conditions should include those that are likely to arise and affect mission success and those that could be exploited by an attack.
  High assurance could require that network protocols and system interfaces are subject to randomly generated faulty input – what is called fuzz testing. Fuzz testing is used by attackers to find vulnerabilities.
  Tests for high assurance could use adversarial knowledge to apply likely attack patterns.
Notes: STUDENT NOTES

## Slide 31: Examples of Late Life Cycle Activities Checks-2
What kind of penetration testing is being done?
  Traditional penetration testing emulates an external attack.
  Penetration testing should be done with the assumption that an adversary has been able to achieve some kind of system access or is a “trusted” insider.
  Penetration testing for high assurance requirements should assume that the adversary is very knowledgeable about the system.
Notes: STUDENT NOTES

## Slide 32: Outline
Open Group: Supply chain provider standard
Open Group: Accreditation: an assurance case
Applying assurance to outsourced development
Assurance: Government regulations and supply chain requirements

## Slide 33: Computing System Supply Chain: Government
Develop In-house
Outsource
Program Office
Prime Contractor
Offshore
Foreign Developers
US
Acquire (COTS)
Acquire
Develop In-House
Outsource
Developer
Reuse
Multiple Developers and Contractors
Developer
Legacy Software
Other Programs
U.S.
Foreign
Global
Firmware that controls electronic hardware is replaced.
Counterfeit hardware
Hardware tampering
Software subject to cyber-attacks
Notes: Let's say the objective is to build a software system.
In this instance, the acquirer has a program office that manages the selection of a prime contractor and monitors the development of the system. The supply chain appears to be simple: program office and prime contractor, but the supply chain for a system acquisition is complex.
The prime contractor has multiple kinds of supply chains. A large system usually includes commercial software products including what we call commercial off-the-shelf or COTS software. Those developers have supply chains.
A prime contractor’s internal software development can be done at multiple locations in the U.S. and offshore.
A prime contractor usually has subcontractors who can be geographically distributed and may have their own supply chains.
It is not unusual for a large system to reuse existing software. But enough time has passed that our knowledge of those efforts is incomplete compared to that for current development.
We also have a collection of supply chain threats. Some of the hardware items could be counterfeit or have been the subject of tampering.
There can be software components with weaknesses that an attacker can exploit to compromise a system, and we have a special class of software called firmware that controls the behavior of electronic devices that might have been replaced.

## Slide 34: Government System Supply Chains
Items of interest include
  components such as microchips used in electronics
  electronic assemblies
  integrated hardware and software devices such as network routers, laptops, and cellphones
  custom software systems and commercial software products
Notes: Our focus is on supply chain risks associated with the acquisition of government information, communications, and technology systems or ICT systems for short. The government is an end point for such supply chains. Hardware products of interest include microchips, electronic assemblies, and integrated hardware-software devices, such as network routers and cell phones. Software supply chains include those for commercial and custom-developed items.

## Slide 35: Government Supply Chain Risks
A key objective for Supply Chain Risk Management (SCRM) is to identify the aspects of a supply chain that are risks.
Management of commercial manufacturing supply chains typically focuses on availability risks: sufficient supply
Systems supply chain risks of interest are those that affect operations and can be instantiated by an active agent. Significant adverse events or threats include
  Inadvertent vulnerabilities created during development
  insertion of counterfeit components or product tampering during manufacture or delivery: Particularly for government systems
Notes: The ICT supply chain risks of interest to us are very different from the risks normally associated with commercial manufacturing. The latter often focuses on inventory management and applies mitigations such as using independent and geographically distributed suppliers. A manufacturing supply chain risk can be a physical event such as an earth quake or flood, or a business event such as supplier bankruptcy.
Rather than resulting from an act of nature or an unexpected business event, ICT supply chain risks are intentional actions by third parties to purposely disrupt the supply chain, compromise the integrity of ICT products, or affect the behavior of deployed ICT systems.
For hardware supply chains, such malicious actions include intentional insertion of counterfeit components or product tampering during manufacture or delivery. The delivered hardware in both cases is not authentic, that is, is not what we ordered or what the manufacturer intended.
Software can be intentionally compromised during development or delivery by third parties, but in most cases, the delivered software is authentic, that is, what the developer intended. We discuss the exceptions in a later chapter. Software supply chain risks are likely unintentional weaknesses created during development, integration, or deployment that enable third parties to purposely compromise an operational system. These errors can occur when the actual operating conditions do not match those assumed by the designers. Some systems are compromised because the designers did not consider how a software feature could be exploited by an attacker.
If we hired a contractor to secure our home, a hardware supply chain risk would be the substitution of an inferior lock for the high-security model we paid for.
As an example of a feature weakness, consider the automobile option that monitors tire pressure. That option uses a wireless network to exchange data among the tire sensors and the dashboard monitor. The design did not consider the possibility that the network could be compromised. It has been demonstrated that a nearby, specially configured automobile can use that network to create a false warning in your car.

## Slide 36: Example of a Counterfeit Threat
Vendor
CISCO
Acquirer
Used source that had access to counterfeit products
Drop-shipped by third party who had it in stock
Government unit receives counterfeit CISCO routers.
Possible enablers:
Purchaser used a vendor that had not been approved for government sales.
Poor vendor supply chain risk management.
Notes: On this slide, we have an example of a substitution of a counterfeit item that occurred during an ICT acquisition. A government agency orders Cisco routers but receives counterfeits. The router boards in the two units are fairly similar. In this case, a closer inspection shows some differences, but, in many instances, it is very difficult to identify counterfeit substitutions.
Counterfeits are a significant acquisition problem. It has been estimated that 10% of government purchases are counterfeit. The DoD, for example, had a counterfeit order of 49,000 chips. In other instances, parts from discarded electronic assemblies have been refurbished and sold as new.

## Slide 37: Examples of Counterfeiting in DoD Supply Chains
The material on the current state of counterfeits in DoD supply chains is drawn from the report, Inquiry into Counterfeit Electronic Parts in the Department of Defense Supply Chain, published by, Committee on Armed Services, United States Senate on May 21, 20121.
  The committee identified 1800 DoD cases of suspect counterfeit parts with the total number of items numbering over 1,000,000.
  These 1800 cases involved over 650 companies each with their own supply chains
  An in-depth history is provided for four of the cases.
  A GAO report on on-line sales of counterfeit parts is included.
1 http://www.gpo.gov/fdsys/pkg/CRPT-112srpt167/pdf/CRPT-112srpt167.pdf
Notes: DoD supply chain failures were analyzed by the Senate Armed Services Committee in 2012. 1800 DoD cases of suspected counterfeit parts were considered which involved 650 companies each with their own supply chains. Our examples are drawn from the four in-depth histories done by the committee

## Slide 38: Senate Report on DoD Counterfeit Incidents
Sources
  The Committee tracked well over 100 of the approximately 1,800 cases of suspect counterfeit parts back through the supply chain.
  More than 70 percent of the suspect parts are traced to China.
  80% of the supply chains started with a U.S supplier.
  Complex supply chains mask the true origin of parts.
    In one case, the part had exchanged hands five times and went through four states and three countries after leaving the original supplier in China before it reached the subcontractor who built the hardware device.
    Contractors were often not aware of the sources of electronic parts.
Notes: The committee tracked well over 100 of those 1800 hundred cases back the source. Over 70% of the suspect parts were traced to China.
It is important to note the following: 80% of the supply chains started with a US supplier; the contractors for electronic assemblies were often not aware of the sources of the parts they procured, and complex supply chains can mask the true origin parts.
In one case, a part that was the cause of system failures had exchanged hands 5 times, passed through four states, and three countries after leaving the original supplier in China. That specific supply chain included an independent distributor which had previously delivered counterfeit parts for other DOD acquisitions. That independent distributor was eventually of prohibited from government procurements.

## Slide 39: Software-based Threats
In the RSA example, the supply chain was secure and the software was authentic.
Software system development and integration
Acquirer
Software component developers
Deployed System
Attack
Enablers:
Inadvertent software weaknesses created during development that enable attacks.
User actions
Software-based threats not considered during system integration

## Slide 40: Firmware: A Special but Important Class of Software-1
Firmware is a set of instructions programmed on a hardware device. It adds functionality to a hardware device and provides the necessary instructions for how the device communicates with the other computer hardware.
All electronic devices such as digital watches, TV remote controls, mobile phones, electronic hotel locks, and disc drives have firmware.
Notes: All electronic devices such as digital watches, remote controls, and DVD drives have software that controls those devices. We refer to that software as firmware which is stored in persistent memory For a DVD drive, firmware controls the rotation of the media, ejects a disc, and controls order in which data is read.
Firmware can have exploitable weaknesses. A software defect in a widely used hotel door lock lets an attacker open any door with a home-made device.

## Slide 41: Firmware: A Special but Important Class of Software-2
On a DVD or CD player such firmware ejects the media, reads the starting locations for the various segments from the media, and manages the physical devices to repeat a section or to randomly play pieces.
Firmware is permanent in the sense that it is stored in read-only memory and can require special updaters to change it.
Exploitable weaknesses can exist in firmware – e.g. a software error in a widely used hotel door lock can be by-passed by with an attacker-constructed inexpensive device.
Notes: All electronic devices such as digital watches, remote controls, and DVD drives have software that controls those devices. We refer to that software as firmware which is stored in persistent memory For a DVD drive, firmware controls the rotation of the media, ejects a disc, and controls order in which data is read.
Firmware can have exploitable weaknesses. A software defect in a widely used hotel door lock lets an attacker open any door with a home-made device.

## Slide 42: Firmware Tampering-1
An attacker can fundamentally change the operation of electronic hardware by changing the firmware that controls it.
Firmware modifications often require physical access to a device even if the device can be accessed remotely.
  Thus the threats and mitigations when physical access is required have considerable overlap with those for hardware.
  Tampering could replace the chip on which the firmware is installed.

## Slide 43: For Government Systems
Common Criteria for Information Technology Security Evaluation (CC) Evaluation of security functions. Required of military systems. http://www.commoncriteriaportal.org/cc/
Supply Chain Risk Management Practices for Federal Information Systems and Organizations: NIST: http://csrc.nist.gov/publications/drafts/800-161/sp800_161_draft.pdf

## Slide 44: US Government Documentation
Federal Information Security Management Act OMB Circular A-130, HSPD-12, FIPS Publication 200
FIPS 199: Standards for Security Categorization of Federal Information and Information Systems
FIPS 200: Minimum Security Requirements for Federal Information and Information Systems
OMB Circular A-130 : Management of Federal Information Resources

## Slide 45: Federal Information Security Management Act (FISMA)
FISMA assigns responsibilities to various agencies to ensure the security of data in the federal government.
Nine Steps
  Categorize the information to be protected.
  Select minimum baseline controls.
  Refine controls using a risk assessment procedure.
  Document the controls in the system security plan.
  Implement security controls in appropriate information systems.
  Assess the effectiveness of the security controls once they have been implemented.
  Determine agency-level risk to the mission or business case.
  Authorize the information system for processing.
  Monitor the security controls on a continuous basis.

## Slide 46: Evaluate Security Functionality
Common Criteria for Information Technology Security Evaluation (CC) is a product assessment of its security properties.
  an international standard
  can be a requirement for non-government systems
  is a US Defense Department Requirement
  documents are available at http://www.commoncriteriaportal.org/cc/

## Slide 47: Common Criteria
The CC permits comparability between the results of independent security evaluations by providing a common set of requirements
  for the security functionality of IT products
  for the assurance measures applied to these IT products during a security evaluation.
Independent laboratories are accredited to perform CC evaluations

## Slide 48: Levels of Assurance-1
A protection profile is the set of security requirements.
CC defines 7 Evaluation Assurance Levels (EAL). For example
  EAL1: Functionally tested
    some confidence in correct operation is required but the threats to security are not viewed as serious
  EAL2: Structurally tested
    delivery of design information and test results,

## Slide 49: Levels of Assurance-2
  EAL3 methodically tested and checked.
    positive security engineering at the design stage without substantial alteration of existing sound development practices.
    coverage of the implementation for a subset of security functionality
    an architectural description of the design developed to understand the security behavior. .
    selective independent confirmation of the developer test results
    vulnerability analysis (based upon the functional specification) of the design.
    security architecture description and guidance evidence provided.

## Slide 50: Levels of Assurance-3
  EAL4 methodically designed, tested, and reviewed.
    based on good commercial development practices which, though rigorous, do not require substantial specialist knowledge, skills, and other resources.
    additional design descriptions,
    coverage of the implementation for the full set of security functionality.
    improved mechanisms and/or procedures that increase the confidence that the product will not be tampered with during development.

## Slide 51: HIPPA
HIPAA, the Health Insurance Portability and Accountability Act, sets the standard for protecting sensitive patient data.
  Any company that deals with protected health information (PHI) must ensure that all the required physical, network, and process security measures are in place and followed.