## Slide 1: Designing Products and Processes Using Six Sigma
Module 7 – Designed Experimentation and Optimization of Product Design Using Response Surface Methodology
SM CMM Integration, IDEAL, Personal Software Process, PSP, SCAMPI, SCAMPI Lead Appraiser, Team Software Process, and TSP are service marks of Carnegie Mellon University.
® Capability Maturity Model, Capability Maturity Modeling, Carnegie Mellon, CMM, and CMMI are registered in the US Patent and Trademark Office by Carnegie Mellon University. For more information on CMU/SEI trademark use, please visit http://www.sei.cmu.edu/about/legal-trademarks.html
Notes: © 2007 Carnegie Mellon University
Title Slide
  Title and Subtitle text blocks should not be moved from their position if at all possible.

## Slide 2
The text and illustrations in this material are licensed by Carnegie Mellon University under a Creative Commons Attribution 4.0 International License.
The Creative Commons license does not extend to logos, trade marks, or service marks of Carnegie Mellon University.
References herein to any specific commercial product, process, or service by trade name, trade mark, manufacturer, or otherwise, does not necessarily constitute or imply its endorsement, recommendation, or favoring by Carnegie Mellon University or its Software Engineering Institute.

## Slide 3: Course Agenda
Day 1
Day 3
Day 2
Day 4
Introduction
Voice of the Customer
KJ Analysis
User Stories and Measures
Analytic Hierarchy Process
KANO Analysis
Y-x Trees
QFD
Requirements and Features
Process Capability Revisited
(Chi-Square, Logistic Regression, Dummy Variable Regression)
Process Optimization
(Monte Carlo Simulation and Optimization)
Process Optimization
(Discrete Event Process Modeling & Simulation)
Robust and Optimized Product Design
(Design of Experiments & Response Surface Methodology)
Day 5
Reliability Growth Test and Modeling
Wrap-up
Notes: © 2007 Carnegie Mellon University
The actual times from each delivery are being collected to arrive at a more precise schedule, but the timings implied by this chart have held true with each delivery thus far.

## Slide 4: Module 7
Critical Parameters Slide 12
Power Consumption Simulator Slide 16
Design of Experiments (DOE) Concepts and Terms Slide 26
Screening Experiment Slide 35
Modeling and Response Surface Methodology Experiments Slide 76

## Slide 5: Permissions Related to Class Tool
Screen shots and other statistical tool information have been used with permission from Minitab, Inc. Information about Minitab software can be found at www.minitab.com.
Minitab is interactive, comprehensive, visual software. It dynamically links statistics with graphics right on your Windows desktop, empowering you to explore data interactively and bring understanding to your organization.
Minitab is a registered trademark or trademarks of Minitab, Inc., in the USA and other countries. ® indicates USA registration.
Other brand and product names are trademarks of their respective companies. Copyright © 2015 Minitab, Inc. All rights reserved.

## Slide 6: Note About Tool Versions
Slides in this module are created with versions of Excel and Minitab that use decimal points for continuous numbers. Some international versions might use commas.

## Slide 7: Learning Objectives
  Understand designed experimentation and how it will assist the Pico laptop team in designing a product that does not overheat and is optimized for minimal power consumption and display brightness
  Apply designed experimentation during product development implementing DFSS (during the “Design” phase of DMADV)
  Use designed experimentation and response surface methodology as tools to model performance of either product design or development processes
  Define an experiment and a model to analyze the Pico power consumption experiment and the display brightness experiment, based on numerous design factors
  Analyze and interpret experimental and optimization outputs related to power consumption
Notes: © 2007 Carnegie Mellon University

## Slide 8
Pico Project Laptop Design Challenge
Notes: © 2007 Carnegie Mellon University

## Slide 9: DMADV Roadmap: Analyze
Phase Exit Review
Define
Measure
Analyze
Design
Verify
Define project scope
Establish CCRs, CTQs, & design goals
Establish formal project
CTQ flowdown: ID potential design drivers
Gather & qualify data
Specify performance bounds
Summarize & baseline data
Explore data; model design dynamics
Focus on significant design drivers
Innovate design alternatives
Select best architecture, design, & feature set
Match design & implementation plans
Reduce design & integration risk
Deliver features using closed loop control
Verify system performance; demonstrate CTQs
Deliver new design
Monitor & learn from users’ experiences (ongoing)
How do changes in the identified factors influence the design functionality and performance measures?
Which factors seem most significant?
Can the impact of the most significant factors be verified?
Beyond technical impacts, do these factor dynamics have financial implications?
What ideas do we have?
Drawing on the ideas, what alternative solution concepts should we consider?
As appropriate for the project scope, what architecture, design, and feature set provide the best balance of
  customer value
  business value
  development and delivery risk?

## Slide 10: DMADV Roadmap: Design
Define
Measure
Analyze
Design
Verify
Define project scope
Establish CCRs, CTQs, & design goals
Establish formal project
CTQ flowdown: ID potential design drivers
Gather & qualify data
Specify performance bounds
Summarize & baseline data
Explore data; model design dynamics
Focus on significant design drivers
Innovate design alternatives
Select best architecture, design, & feature set
Match design & implementation plans
Reduce design & integration risk
Deliver features using closed-loop control
Verify system performance; demonstrate CTQs
Deliver new design
Monitor & learn from users’ experiences (ongoing)
How will the design work be organized and managed?
How will development and support costs impact product net value?
Considering the design and implementation plans, what risks can be anticipated and mitigated while there is still flexibility?
Comparing predictions and data during development,
  Is the emerging product performance being tuned and optimized?
  Is the development process on track?
Phase Exit Review

## Slide 11: Design Challenge Facing the Pico Team
The Pico laptop team is now facing a critical design challenge: to design the next-generation laptop to run for long duration without overheating and to consume minimal power.
During the “Define” and “Measure” phases in DMADV (including the Voice of the Customer activity, KJ analysis, and QFD), a number of critical-to-quality (CTQ) parameters were identified, including overheating and power consumption.
Both will be treated as formal CTQ parameters to predict, track, and manage during development. Duration will be measured in wall-clock hours, and power consumption will be measured on a scale of watts of power. The desire will be to identify a design that runs a long time without overheating and a design that uses minimal watts of power during normal operation.

## Slide 12: Critical Parameters Driving Overheating
The Pico team used Y-to-x analysis conducted earlier in the DMADV process to identify 12 critical parameters potentially driving overheating.
  Digital I/O bandwidth (20 to 2100 Mbit/seconds possible)
  Percent recyclable content (0 to 80% possible)
  Impact of security software measures (0 to 100% possible)
  Weight (2 to 9 pounds possible)
  Size in volume (25 to 150 cubic inches)
  Display brightness (200 to 2000 lumens)
  Processor speed (1 to 6 gigahertz)
  Humidity (0 to 90 percent)
  Temperature (10 to 150 degrees F)
  Degree of software caching (0 to 100 percent)
  Lead-free design (yes, no)
  Operating system (Windows, Linux)

## Slide 13: Critical Parameters Driving Power Consumption
The Pico team used the Y-to-x analysis conducted earlier in the DMADV process to identify seven critical parameters potentially driving power consumption.
  Processor speed (1 to 10 gigahertz)
  Impact of security software measures (1 to 100% possible)
  Weight (2 to 9 pounds possible)
  Size in volume (25 to 150 cubic inches)
  Display brightness (200 to 2000 lumens)
  Humidity (0 to 90%)
  Temperature (10 to 150 degrees F)
Note that because overheating and power consumption are related, they share some common critical parameters.

## Slide 14: What Would Your Development Team Do?
Copy the approach used on the last product development?
Single out the op 1-2 critical parameters and figure out the best solution in terms of these few parameters?
Evaluate all possible scenarios of the 12 critical parameters for overheating? (Assuming three settings on each of 12 parameters would represent 531,441 scenarios to evaluate.)
Evaluate all scenarios of the 7 critical parameters for power consumption? (Assuming a high-medium-low setting on each of 7 parameters would represent 2,187 scenarios to evaluate.)
Try changing one parameter at a time to see if a desirable or optimum solution is achievable?
Perform a designed experiment, and let statistics save you time and energy!

## Slide 15
The Pico Laptop Power Consumption Simulator
Notes: © 2007 Carnegie Mellon University

## Slide 16: The Pico Laptop Power Consumption Simulator
Development teams often find themselves facing a critical decision.
  Invest in a series of physical and/or software prototypes.
OR
  Build a simulator for design performance.
Either option may be quite expensive,and both consume precious schedule time.
The Pico team decided to build a simulator for power consumption based on the 7 critical parameters they identified.
You will use this simulator to assist in identifying which critical parameters drive longer durations without overheating.
Open Power Consumption-Simulator-v010.xls

## Slide 17: Concept and Use of the Power Consumption Simulator
The simulator is a Microsoft Excel spreadsheet that has all cells protected except the input cells corresponding to the 7 possible critical factors. Note that the simulator should only be provided valid values for the scale of each factor and zeros for rows in which scenarios are not to be evaluated.

## Slide 18: Concept and Use of the Simulator
The simulator is programmed to handle up to 50 scenarios (rows) with each scenario evaluated for Power Consumption twice (two replications).

## Slide 19
Class Exercise 1: Informal Attempt to Screen Critical Factors
Notes: © 2007 Carnegie Mellon University

## Slide 20: Class Exercise 1
To help demonstrate the efficiencies gained by screening design of experiments, students will use the simulator informally to identify which critical parameters are most important for increasing laptop hours of operation without overheating.
  Students will get three minutes to use the simulator, at which time the lease on the simulator will end.
  Students will share their answers with the class after the time has elapsed.
  Student names and answers will be recorded on the flip pad at the front of the class for reference later.

## Slide 21: Class Exercise 1 Initial Debrief
Remember, in real life, simulators take much longer to set up, run, and analyze the outputs. You should think of each scenario processed in this simulator as a schedule hit of days or weeks.
What are the critical factors to further study with regard to hours of operation without overheating?
How much longer would you need to find an answer?
Would you be confident of your answer?

## Slide 22
Class Exercise 2: Informal Attempt to Optimize Design on Power Consumption
Notes: © 2007 Carnegie Mellon University

## Slide 23: Class Exercise 2
To help demonstrate the efficiencies gained by design of experiments and response surface methodology, students will first be asked to use the simulator informally to identify an optimal solution (minimum power consumption) for the Pico laptop team.
  Students will get five minutes usage on the simulator, at which time the lease on the simulator will end.
  Students will share their optimal values of power consumption but keep secret their settings of the critical factors.

## Slide 24: Class Exercise 2 Initial Debrief
Remember, in real life, simulators take much longer to set up, run, and analyze the outputs. You should think of each scenario processed in this simulator as a schedule hit of days, weeks, or even months.
What was the lowest power consumption reached?
How much longer would you need to find a better solution?
Would you be confident of your solution?

## Slide 25
Introduction to Design of Experiments (DOE) and Response Surface Methodology (RSM)
Notes: © 2007 Carnegie Mellon University

## Slide 26: What Is Design of Experiments?
Design of experiments (DOE) can be thought of as a fancy way to identify and collect a sample of data (x factors and a y outcome), enabling the determination of a quantified, predictive relationship between the x factors and the y outcome.
DOE is probably the most powerful and business-impacting statistical technique within the field of quality and Six Sigma. Using what are called “fractional factorial” experimental designs, predictive relationships may be identified with a very small set of data. “Fractional factorial” designs require only a subset of combinations of the various factors – and thus are very efficient!
Designed experiments provide an efficient approach to solving product design decisions but can also be used to develop effective CMMI process performance models.
Both purposes serve to make an organization more successful and profitable.

## Slide 27: When Should DOE Be Used?
DOE should be used when
  several controllable factors exist that influence the outcome
  controllable factors have interaction effects on the outcome
  there is not enough resources to exhaustively evaluate all possible combinations of the factor settings

## Slide 28: What Is Response Surface Methodology (RSM)?
RSM is an approach that builds on DOE and uses intelligent algorithms to conduct a series of experiments to define a prediction equation for the outcome responses and to find an optimal solution for the outcome based on systematic control of various factor settings.
Response surface may be thought of as the surface representing the response values at all of the different settings of the factors.
Complicated, real-life situations often have nonlinear surfaces with valleys, hill-tips, and saddles—similar to terrain seen on a topographic map.
Although we will not get into the theory, RSM optimization uses intelligent and efficient algorithms for searching and finding maximums and minimums on response surfaces. The statistical package will conduct this activity behind the scenes for us.

## Slide 29: When Should RSM Be Used?
RSM should be employed when an optimal solution is desired and a straightforward analytical solution is not practical.
RSM is especially helpful when several experimental factors have an interaction on the outcome.

## Slide 30: Types of Design of Experiments
Generally, there are three types of designed experiments.
Screening Designs – designed experiments focused on evaluating a large number of potential factors to quickly determine which factors warrant further study in a modeling design. (Exercise 1)
Modeling Designs – designed experiments focused on modeling pertinent factors and establishing a predictive equation for the outcome. (Exercise 2)
Optimization Designs – designed experiments focused on determining an optimal solution for the outcome based on identified settings of the factors. (Exercise 3)

## Slide 31: Our Approach to Teaching DOE and RSM
Instead of teaching the theory and formulas behind the methods, we will capitalize on the user-friendly capabilities of a modern statistical package, called Minitab, to teach you how to do a designed experiment.
DOE and RSM are the subject of a series of undergraduate and graduate courses in college and Six Sigma Black Belt curriculums.
Our intent is to present the subject simply and teach you, as a practitioner, how to use a tool to conduct a simple designed experiment and optimization for either a product design or process solution.

## Slide 32: Terms and Concepts – 1
Runs
A row of a DOE matrix that depicts a scenario implementing the settings for the x factors (critical parameters) and the corresponding response or outcome value.
Aliasing
When two or more factors can not be discerned from each other in a designed experiment because they each receive the same high-medium-low settings on each run of an experiment.
Interaction Terms
Additional factors that may be added to the designed experiment representing the multiplicative product of two or more of the primary factors. Interaction terms may be thought of as the interactions of two drugs. Individually, each drug may help, but when used together, they can cause an adverse effect!

## Slide 33: Terms and Concepts – 2
Resolution of the Experiment
Designed experiments have different resolutions, which can be thought of as residing on a magnification scale. The four following resolutions are often encountered in practice.
  Resolution II – A designed experiment that is so weak in information that it has aliasing of primary factors with each other (weakest).
  Resolution III – A designed experiment that is slightly stronger. Primary factors are not aliased with each other but are aliased with 2-way interactions.
  Resolution IV – A designed experiment that is even stronger. Primary factors are not aliased with each other, or with the 2-way interactions, but allow 2-way interactions to be aliased with each other.
  Resolution V – A designed experiment that is even stronger. There is no aliasing among primary factors nor 2-way interactions.

## Slide 34: Terms and Concepts – 3
Replications
Each row of a DOE matrix can be evaluated more than once for a response or outcome value. Thus, a replication of one implies that the scenario or run will be evaluated twice for a response value. This allows the variability within a scenario to be evaluated and supports our analysis of deciding which factors are significant in the prediction model.
(Note that each simulator you will work with provides two response values to a given scenario in the experiment, so we will have two replications.)
Repetitions
This concept is slightly different from replication in that multiple measures are taken at the same settings without the need to reset any factors between the multiple measures. Replications presume that the activity of resetting the factors physically, including any equipment resetting, occurs between each of the multiple measures.

## Slide 35
Minitab Support of Designed Experiments for Screening Significant Factors
Notes: © 2007 Carnegie Mellon University

## Slide 38: Screening Experiment Process
Define the response and experimental factors
Define the experimental model and “run budget”
Check the design of the experiment created by JMP
Run the experiment
Launch the analysis of the experiment
Examine the analysis and determine the solution
Set the random seed to the value of “10” and click OK.

## Slide 41: Screening Experiment Process
Define the response and experimental factors
Define the experimental model and “run budget”
Check the design of the experiment created by JMP
Run the experiment
Launch the analysis of the experiment
Examine the analysis and determine the solution

## Slide 50: Screening Experiment Process
Define the response and experimental factors
Define the experimental model and “run budget”
Check the design of the experiment created by JMP
Run the experiment
Launch the analysis of the experiment
Examine the analysis and determine the solution

## Slide 55: Screening Experiment Process
Define the response and experimental factors
Define the experimental model and “run budget”
Check the design of the experiment created by JMP
Run the experiment
Launch the analysis of the experiment
Examine the analysis and determine the solution

## Slide 61: Screening Experiment Process
Define the response and experimental factors
Define the experimental model and “run budget”
Check the design of the experiment created by JMP
Run the experiment
Launch the analysis of the experiment
Examine the analysis and determine the solution

## Slide 68: Screening Experiment Process
Define the response and experimental factors
Define the experimental model and “run budget”
Check the design of the experiment created by JMP
Run the experiment
Launch the analysis of the experiment
Examine the analysis and determine the solution

## Slide 75: Final Debrief of Exercise 1
Did you accurately identify the significant factors before we did the screening DOE? Were you lucky?
What resolution experiment did we just run?
What does this resolution provide us and not provide us?
What resolution would you prefer to have if you want to provide the Pico laptop team with a solid answer on the factors driving duration without overheating?
What could your next steps be?

## Slide 76
Minitab Support of Designed Experiments and Response Surface Methodology for an Optimized Solution
Notes: © 2007 Carnegie Mellon University

## Slide 135
If you had four x factors and two outcome factors, you would need to construct this graph for each different possible pairings of the x factors to conclude settings for optimizing the two outcome factors!!!

## Slide 136: Final Debrief for Exercise 2
What are the optimal design settings to have minimal power consumption for the Pico laptop?
What is the minimal power consumption level predicted by the experimental model?
Who came closest to the optimal settings and answer for power consumption?
Knowing that the power consumption is not a flat plane response surface for the different factor settings, would you care about sensitivity analysis around your optimal settings, just in case the Pico laptop team can only come close on some of the settings?

## Slide 137: Optional Independent Student Exercise
Based on the handout with instructions for an additional exercise and the CDROM of a separate simulator for hours without overheating, conduct a screening experiment, followed by a modeling experiment and a response surface analysis, to identify alternative optimums for key scenarios outlined in the handout.

## Slide 138
Summary
Notes: © 2007 Carnegie Mellon University

## Slide 139: Summary
Designed experimentation and response surface methodology enabled the Pico team to quickly and efficiently determine an optimal laptop design for power consumption.
These two methods can be taught and used by practitioners without the need to teach the underlying theory and equations.
Product designers and process improvement champions should consider using these two methods to develop optimal solutions.
The Pico team is well positioned to finish development and move into the “Verify” phase of DMADV.
Notes: © 2007 Carnegie Mellon University

## Slide 140
Questions?
Notes: © 2007 Carnegie Mellon University